## Slide 1: CTS 6319 Cyber Security: Measurement and Data Analysis
Dr. Elias Bou-Harb
ebouharb@fau.edu EE 503B
Office hours: Mondays 4-6pm

## Slide 2: Material
On Canvas
  OSI/TCP/IP (for Lecture 2)
  TCP/IP: Reading Except Chapter 6 (for Lecture 2)
  Networking 101: Very good read
  Research Paper: Can We Identify NAT Behavior by Analyzing Traffic Flows?

## Slide 3: Networking 101
Open system interconnection (ISO/OSI reference model)
  Data communication standards
  Defines processes and tasks of network hosts
  A layered Architecture
    Easier to understand
    Easier to debug
    Easier to expand

## Slide 4
Networking 101
All
People
Seem
To
Need
Data
Processing

## Slide 5: Networking 101
Application layer
  The 7th layer
  End-User Interaction
  Application layer protocols
  Name a few?

## Slide 6: Networking 101
Presentation layer
  The 6th layer
  Helps map application layer protocols to lower level layers
  Provides common formats that the lower levels can understand
  Compression/Encryption of application information is accomplished

## Slide 7: Networking 101
Session layer
  The 5th layer
  Establishes the concept of a session between two communicating hosts
    Crucial for network investigation
      Mapping of sessions
      Measuring traffic/protocols/anomalies
  Could be considered as virtual connections between applications

## Slide 8: Networking 101
Transport layer
  The 4th layer
  Decision between connection-oriented and connectionless
  Various functionalities
    Segmentation
    Error control
    Multiple session handling

## Slide 9: Networking 101
Network layer
  The 3th layer
  Provides logical addressing to route packets
  Routing algorithms
  Buffering and queuing theories
  Encapsulated data into the notion of packets

## Slide 10: Networking 101
Data-link layer
  Allows devices to access the network
  Introduces the concept of physical addresses
  Prepares data to be sent over network media
  Adapts to the physical medium

## Slide 11: Networking 101
Physical layer
  Deals with putting the frame on the wire
  Establishes hardware requirements

## Slide 12: Networking 101-The big picture

## Slide 13
Networking 101-Relation to TCP/IP
OSI
TCP/IP

## Slide 14
Networking 101- TCP/IP Model
  A DoD initiative
  Realizes the ISO/OSI Model
  Network Reliability, a main concern

## Slide 15
Networking 101- TCP/IP Model & Protocols

## Slide 16
Networking 101- DNS

## Slide 17
Networking 101- DNS

## Slide 18
Networking 101- DNS

## Slide 19
Networking 101- DNS
DNS Query Type
ANY ??

## Slide 20
Networking 101- DHCP
  Dynamic Host Control Protocol
  Permits automatic IP configuration assignment to network hosts
    IP address
    Default Gateway
    DNS Servers
    Etc..

## Slide 21
Networking 101- DHCP

## Slide 22
Networking 101- DHCP
  Dynamic Host Control Protocol
  Permits automatic IP configuration assignment to network hosts
    IP address
    Default Gateway
    DNS Servers
    Etc..

## Slide 23
Networking 101- UDP
  User Datagram Protocol
  Connectionless, non-guaranteed
  Does not offer retransmission for reliable delivery, packetization and reassembly, flow control, congestion avoidance, etc.
  No session setup
  Forces the application to handle errors
  Fast, often used for real-time applications

## Slide 24
Networking 101- TCP
  Transport Control Protocol
  Connection-oriented, guaranteed delivery
  Offers retransmission, packetization and reassembly, flow control, congestion avoidance, etc.
  Session establishment/termination, packets’ acknowledgement

## Slide 25
Networking 101- TCP Header

## Slide 26
Networking 101- IP Header

## Slide 27
Networking 101- IP Header

## Slide 28: Networking 101- IP addressing

## Slide 29: Networking 101- Recall Binary<->Decimal
What is 40 in binary?
What is 01011010 in decimal?

## Slide 30: Networking 101- IP addressing
Private IP addresses
  Used only in local area networks
  Do not have to be paid for
  Ranges:
        192.168.0.0->192.168.255.255
        172.16.0.0->172.31.255.255
        10.0.0.0->10.255.255.255
Public IP addresses
  Routable, Internet-accessible
  Allocated by the Internet Assigned Numbers Authority (IANA)

## Slide 31
Networking 101- IP NAT/PAT
  Network address translation/Port address translation
  Allow internal hosts to access Internet services using 1 (or few) public IP addresses
    Can be generalized to access any network from another network
  Procedure: Source IP address is substituted with NAT Router IP address
        Source Port is saved in NAT Router to be used in reply packets
  https://tools.ietf.org/html/rfc2663 RFC Documentation

## Slide 32: HTTP Packets

## Slide 33: Telnet Packets
TCP packets?

## Slide 34: TCP 3-way Handshake

## Slide 35: Telnet Packets
TCP packets?

## Slide 36: DHCP Packets

## Slide 37: DNS Packets

## Slide 38
?

## Slide 39
?

## Slide 40
?

## Slide 41: To Do:
Play around with Wireshark (https://www.wireshark.org/)
Download sample packets (.pcap) files from https://wiki.wireshark.org/SampleCaptures
More Stuff!
MALWARE ANALYSIS AND INCIDENT RESPONSE TOOLS FOR THE FRUGAL AND LAZY (http://postmodernsecurity.com/2015/09/11/malware-analysis-and-incident-response-tools-for-the-frugal-and-lazy/)
More tools (http://www.gfi.com/blog/the-top-20-free-network-monitoring-and-analysis-tools-for-sys-admins/)
Traffic analysis libraries (http://jnetpcap.com/, http://www.pcap4j.org/) (http://www.tcpdump.org/, http://research.wand.net.nz/software/libtrace.php)

## Slide 42
http://faculty.eng.fau.edu/ebouharb/
Dr. Elias Bou-Harb
ebouharb@fau.edu EE 503B
Office hours: Mondays 4-6pm
CTS 6319 Cyber Security: Measurement and Data Analysis